## Slide 1: Materials Manufacturing (EDPT 601)
Tutorial 3 ( Metal Forming Processes)
Sheet metal forming
By: Eng. Sherifa Taher

## Slide 2: Classification of metal forming processes

## Slide 3: Sheet metal forming processes
Bending
It is the process of deforming or straining of a sheet metal around a straight or linear axis to take a permanent bend.
The sheet metal is subjected to compression (on inside of neutral plane) as well as tension (on outside of neutral plane)

## Slide 4: Types of bending
1. V-bending | 2. Edge bending | 3. Air bending
For low production Simple and inexpensive | For high production Dies are more complicated and costly Requires pressure pad | Flexible and requires relatively low forces Less precise than other bending operations.

## Slide 5: Types of bending
4. Roll bending | 5.Roll forming | 6. Seaming
Continuous process For sheets, pipes, plates and beams. | Transforms flat sheets into complex sections through progressive bending operations. | Commonly used in food industry on canned foods and used in automotive industry.

## Slide 6: Spring-back
also known as elastic recovery, is the result of metal tending to return to its original shape after undergoing compression and tension (stretching).
Reasons: when bending pressure is removed, elastic energy remains in bent part, causing it to recover partially towards its original shape.

## Slide 7: 2. Shearing
There are several operations performed based on shearing:
Piercing (punching)
Blanking
Perforating
Parting
Notching
Lancing
Slitting
Nibbling

## Slide 8: Piercing and blanking
Blanking: Sheared slug (part) is the required
part and the rest of the sheet is discarded as scrap
Piercing (Punching): Sheared slug (part) is
discarded as scrap.

## Slide 9
Perforating Punching a number of holes in a sheet. | Parting Shearing the sheet into two or more pieces. | Notching Removing pieces from the edges.
Lancing Portion of a hole is cut while the remaining is bent to a desired shape. | Slitting Shearing operation using circular blades that follow straight or circular paths. | Nibbling Shearing process that utilizes series of overlapping cuts to make complex shapes.

## Slide 10: Punching dies

## Slide 11: 3. Deep drawing
A flat blank is formed into a cup by forcing a punch against the center portion of a blank that rests on a die ring.

## Slide 12: Deep drawn products

## Slide 13: Shearing and deep drawing dies
Clearance between punch and die is greater than material thickness

## Slide 14: Deep drawing defects
Flange wrinkling: small holding force.
Wall wrinkling: insufficient holding force, wrinkling initially occurring on the flange.
Tearing: high stress and sharp die corners.
Earing: anisotropy of the material.
Surface scratches: Die or punch not having a smooth surface, insufficient lubrication.