## Slide 1: Materials Manufacturing (EDPT 601)
Tutorial 7
Machining
By: Eng. Olivia Nashaat

## Slide 2: Machining
Machining is a material removal process in which a sharp cutting tool is used to mechanically cut away material so that the desired part geometry remains.
Cutting action involves shear deformation of work material to form a chip.
A cross‑sectional view of the machining process

## Slide 3: Machining Operations
Most important machining operations:
  Turning
  Drilling
  Milling

## Slide 4: Turning
Turning is the process of machining cylindrical and conical surfaces
It is usually performed on a lathe where the workpiece is rotated into a longitudinally fed, single point cutting tool.

## Slide 5
Other important turning operations include:
  Facing
  Parting (cutting off)
  Threading
  Grooving
  Taper turning
  Chamfering
  Form turning (profiling)
  Knurling
  Drilling

## Slide 6
Facing | Parting (Cut Off) | 
Threading | External Grooving | 

## Slide 7
Taper Turning | Chamfering | 
Boring and Internal Grooving | Drilling | 

## Slide 8: Common Turing tools

## Slide 9
Facing Side turning Chamfering
(RH/LH facing tool or bent tool) (RH or LH side tool) (Bent tool )
Cornering parting off Threading
(corner tool) (Cut-off tool) (Threading tool)

## Slide 10
Drilling creates a round hole in a workpiece
It is performed on a drill press using a drill/drill bit.
Drilling

## Slide 11
Operations that can be performed on a drill press are:
  Drilling
  Core drilling
  Step drilling
  Counter-boring
  Counter-sinking
  Reaming
  Center drilling
  Gun drilling

## Slide 12: Milling
Milling is the process of machining flat, curved or irregular surfaces by feeding the workpiece against a rotating cutter containing a number of cutting edges.

## Slide 13: Conventional and climb milling
Conventional milling is the common type of milling. There may be a tendency for the tool to chatter and the workpiece to be pulled upward, necessitating proper clamping. It is also called slab/up milling.
In climb milling, also called down milling, the downward component of the cutting forces holds the workpiece in place.

## Slide 14: Milling Operations
Milling operations include:
Slab milling
Face milling
End milling
Straddle milling
Form milling
Slitting
Slotting

## Slide 15
Slab milling | Face milling | 
End milling | Straddle Milling | 

## Slide 16
Form milling | Slitting | 
Slotting | T-slot Cutting |